## Slide 1: IP addresses and network interfaces
U1-W12-L01 · 1/8 · Content CC BY 4.0 / code MIT
Unit 1 · Week 12 · Lesson 1
Interpret IPv4 and IPv6 addresses and their roles.
Notes: Learning intention
Suggested time: 2 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
Explain the goal and the expected independent outcome. Interpret IPv4 and IPv6 addresses and their roles. This is ungraded textbook learning. Suggested times can be adjusted to the class. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF

## Slide 2: Retrieval and explanation
U1-W12-L01 · 2/8 · Content CC BY 4.0 / code MIT
Which device role moves packets between networks?
Which layer uses IP?
Notes: Individual retrieval, then partner comparison
Suggested time: 5 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
A router performs IP forwarding between networks. IP belongs to the Internet layer in the DoD model. Allow silent thinking before discussion. Ask a learner to justify an answer before revealing the explanation. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF

## Slide 3: Address families
U1-W12-L01 · 3/8 · Content CC BY 4.0 / code MIT
Feature | IPv4 | IPv6
Length | 32 bits | 128 bits
Common notation | Four decimal groups | Hexadecimal groups
Example context | 192.168.40.12 | 2001:db8::12
Identifies | Network interface | Network interface
Notes: Worked table and teacher explanation
Suggested time: 6 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
An interface can have multiple addresses. Do not describe an IP as a permanent unique label for an entire person or device. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF

## Slide 4: An interface address
U1-W12-L01 · 4/8 · Content CC BY 4.0 / code MIT
Read 192.168.40.12 as four decimal groups.
Each group ranges from 0 to 255.
The /24 describes the network-prefix length.
Notes: Predict, model and explain
Suggested time: 10 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
Keep address and prefix separate. The larger IPv6 space follows from its larger address length, not from hexadecimal notation alone. Pause for predictions before discussing the expected result. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF

## Slide 5: Address claims
U1-W12-L01 · 5/8 · Content CC BY 4.0 / code MIT
Explain why 192.168.40.300 is invalid IPv4 text.
Compare a numeric address with a website name.
Notes: Guided paired practice
Suggested time: 10 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
300 exceeds one octet’s range. A website name is not an IP address, though DNS may provide address records for it. Swap explaining and checking roles so both learners articulate the reasoning. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF

## Slide 6: Independent practice
U1-W12-L01 · 6/8 · Content CC BY 4.0 / code MIT
Compare IPv4 and IPv6 without copying the table.
Explain address, interface and prefix.
Give one invalid IPv4 example and its reason.
Notes: Independent application with optional support
Suggested time: 12 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
Check 32 versus 128 bits, correct common notation and a reasoned invalid-octet example. Use only synthetic examples. Offer the relevant worked example if needed, then use a changed case to check independent understanding. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF

## Slide 7: A choice to explain
U1-W12-L01 · 7/8 · Content CC BY 4.0 / code MIT
IPv6 has a larger address space mainly because it uses
A: 128 bits instead of 32.
B: letters instead of decimal digits.
Notes: Whole-class response and justification
Suggested time: 5 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
A. Notation represents values. Address length determines the number of available bit patterns. Give thinking time and collect reasons, without recording scores. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF

## Slide 8: Exit explanation
U1-W12-L01 · 8/8 · Content CC BY 4.0 / code MIT
Explain the role of an IP address.
State why its subnet information also matters.
Notes: Individual reflection and fresh explanation
Suggested time: 5 minutes.
Prepare: Open the addressing chapter and its learning resources. Use paper or a local editor as appropriate, with fictional data and disposable practice copies. The suggested 55-minute lesson is flexible.
It identifies an interface for IP communication. The sender uses its mask/prefix to judge whether a destination is local. Use the response to select the next explanation or practice activity. Teaching reference: https://edugenio.github.io/cs-atar-textbook/#addressing. Technical/course references: https://www.rfc-editor.org/rfc/rfc1122 https://www.rfc-editor.org/rfc/rfc1918 https://senior-secondary.scsa.wa.edu.au/__data/assets/pdf_file/0003/1090875/Year-11_12_Computer-Science_ATAR_Additional-syllabus-support-booklet-.PDF